## Slide 1
Internal Architecture
Of
8086 Microprocessor
Course ID: CSE - 341
Course Title: Microprocessors
Department of Computer Science & Engineering BRAC University.

## Slide 2: Lecture References:
Book:
  Microprocessors and Interfacing: Programming and Hardware, Chapter # 2, Author: Douglas V. Hall
CSE – 341 : Microprocessors
BRAC University

## Slide 3: Organization of the 8086
Microprocessor 8086 is internally divided into two separate functional units. These are:
    Bus Interface Unit (BIU)
    Execution Unit (EU).
These two functional units can work simultaneously to increase system speed and hence the throughput.
Throughput is a measure of number of instructions executed per unit time.
These two units interact directly with each other through Internal Bus.
CSE – 341 : Microprocessors
BRAC University

## Slide 4: 16-Bit 8086 Intel Processor Architecture
CSE – 341 : Microprocessors
BRAC University
Physical address = segment no x 10h + offset
MOV AX,3H MOV BX,4H
ADD AX,BX
ADD AX, 2H
AX
BX
ADD

## Slide 5: Bus Interface Unit
BIU: facilitates communication between the EU & the memory or I/O circuits. It provides a full 16-bit bi-directional data bus and 20-bit address bus.
  Responsible for transmitting addresses, data, and control signals on the buses.
  Registers (CS, DS, ES, SS, and IP) hold addresses of memory locations.
  IP (instruction pointer) contain the address of the next instruction to be executed by the EU.
CSE – 341 : Microprocessors
BRAC University

## Slide 6: Bus Interface Unit
The bus interface unit is responsible for performing all external bus operations, as listed below.
  It sends address of the memory or I/O.
  It fetches instruction from memory.
  It reads data from port/memory.
  It Writes data into port/memory.
  It supports instruction queuing.
  It provides the address relocation facility.
CSE – 341 : Microprocessors
BRAC University

## Slide 7: Physical Address Calculation in BIU
CSE – 341 : Microprocessors
BRAC University
To generate 20 bit physical address Segment Registers (CS, DS, SS, ES) and Pointer and Index Registers (IP, SP, BP, SI, DI) are needed.

## Slide 8: Memory Segment and Segment Registers
CSE – 341 : Microprocessors
BRAC University

## Slide 9: Physical Address Calculation Examples
CSE – 341 : Microprocessors
BRAC University

## Slide 10: Physical Address Calculation Examples
CSE – 341 : Microprocessors
BRAC University

## Slide 11: Instruction Queue
To speed up program execution, the BIU fetches six instruction bytes ahead of time from the memory.
These prefetched instruction bytes are held for the execution unit in a group of registers called Queue.
With the help of queue it is possible to fetch next instruction when current instruction is in execution.
The queue operates on the principle first in first out (FIFO). So that the execution unit gets the instructions for execution in the order they are fetched.
Exceptions: JUMP and CALL instructions
CSE – 341 : Microprocessors
BRAC University

## Slide 12: Instruction Queue
CSE – 341 : Microprocessors
BRAC University
38AB0
38AB4
38AB5
38AB6
38AB3
38AB2
38AB1
Current Instruction in EU
Instructions prefetched
in Queue
49520
49521
49522
49523
By JUMP or CALL
IP
IP
CALL ADDITION

## Slide 13: Instruction Queue
CSE – 341 : Microprocessors
BRAC University
Fig: Pipelining

## Slide 14: Execution Unit (EU)
The execution unit of Internal Architecture of 8086 tells the BIU from where to fetch instructions or data, decodes instructions and executes instructions. It contains
  Control Circuitry
  Instruction Decoder
  Arithmetic Logic Unit (ALU)
  Flag Register
  General Purpose Registers
  Pointers and Index Registers
CSE – 341 : Microprocessors
BRAC University

## Slide 15: Execution Unit (EU)
The main components of the EU are General purpose registers, the ALU, Special purpose registers, Instruction Register and Instruction Decoder and the Flag/Status Register.
Fetches instructions from the Queue in BIU, decodes and executes arithmetic and logic operations using the ALU.
Sends control signals for internal data transfer operations within the microprocessor.
Sends request signals to the BIU to access the external module.
It operates with respect to T-states (clock cycles) and not machine cycles.
CSE – 341 : Microprocessors
BRAC University

## Slide 16: Arithmetic Logic Unit (ALU)
  This unit performs all arithmetic and logical computations.
  Instructions those are fetched and decoded, are executed in the ALU
  Thus, ALU has direct access to General Purpose Registers and Flags.
CSE – 341 : Microprocessors
BRAC University

## Slide 17: Temporary and Flag registers
  Every processor has some temporary registers those are not visible to the programmers.
  For these registers, our data are not lost in between different kinds of operations,
    XCNG CX, BX
        MOV temp, CX
        MOV CX, BX
        MOV BX, temp
        FLAG Registers: A flag is a flip–flop which indicates some condition produced by the execution of an instruction or controls certain operations of the EU.
CSE – 341 : Microprocessors
BRAC University

## Slide 18: Thank You !!
CSE – 341 : Microprocessors
BRAC University