## Slide 1: Dept. of Computer Science and Engineering BRAC University CSE 341 Team
8086 Addressing Modes

## Slide 2: Lecture References:
Book:
  Microprocessors and Interfacing: Programming and Hardware, Chapter # 2, Author: Douglas V. Hall
  The 8086/8088 Family: Design, Programming, And Interfacing, Chapter # 2, Author: John Uffenbeck.

## Slide 3: Addressing Mode and Categories
The different ways in which a microprocessor can access data are referred to as its addressing modes.
Addressing modes of 8086 Microprocessor are categorized as:
    Addressing Data
    Addressing Program codes in memory
    Addressing Stack in memory
    Addressing I/O
    Implied addressing

## Slide 4: Things to know…
Instruction format
Instructions can have 1, 2 or no operands
    INC AX ; 1 operand
    ADD CX, DX ; 2 operands CX = CX + DX
    HLT ; no operand
Instruction cannot have:
    SUB [DI], [1234h] ; memory locations as both operands
    MOV 1234, AX ; immediate data as destination operand
opcode
Operand(s)
Destination source

## Slide 5: 1. Addressing Data
  Immediate addressing
  Direct addressing
  Register [direct] addressing
  Register indirect addressing
  Base-plus-index addressing
  Register relative addressing
  Base-relative-plus-index addressing

## Slide 6: 1. Addressing Data
Immediate addressing
  Data is immediately given in the instruction
  MOV BL, 11
Direct addressing
  Data address is directly given in the instruction
  MOV BX, [437AH]
b
h
d

## Slide 7: 1. Addressing Data
Register [direct] addressing
  Data is in a register (here BX register contains the data)
MOV AX, BX
Register [indirect] addressing
  Register supplies the address of the required data
MOV CX, [BX]
MOV AL, BX

## Slide 8: 1. Addressing Data
Base-plus-index addressing
  Base register is either BX or BP
  Index register is either DI or SI
  MOV DX, [BX+DI]
Register relative addressing
  Register can be a base (BX, BP) or an index register (DI, SI)
  Mainly suitable to address array data
  MOV AX, [BX+1000]

## Slide 9: 1. Addressing Data
Base-relative-plus-index addressing
  Suitable for array addressing
  MOV AX, [BX+DI+10]

## Slide 10: 2. Addressing Program Codes in Memory
Used with JMP and CALL instructions
3 distinct forms:
  Direct
  Indirect
  Relative

## Slide 11: 2. Addressing Program Codes in Memory
Address is directly given in the instruction
JMP 1000: 0000
JMP doagain ; doagain is a label in code
CALL 1000:0000
CALL doagain ; doagain is a procedure in code
Often known as far jump or far call
CS IP

## Slide 12: 2. Addressing Program Codes in Memory
Address can be obtained from
  a) any GP registers (AX,BX,CX,DX,SP,BP,DI,SI)
      JMP AX
  b) any relative registers ([BP],[BX],[DI],[SI])
      JMP [BX]
  c) any relative register with displacement JMP [BX + 100h]
IP = AX ; then CS : IP
IP = what is inside the physical address of DS : BX ; then CS : IP
IP = what is inside the physical address of DS : BX +100h ; then CS : IP

## Slide 13: 3. Addressing Stack in Memory
PUSH and POP instructions are used to move data to and from stack (in particular from stack segment).
        PUSH AX
        POP CX
CALL also uses the stack to hold the return address for procedure.
        CALL SUM ; SUM is a procedure name

## Slide 14: 4. Addressing Input and Output Port
IN and OUT instructions are used to address I/O ports
Could be direct addressing
  IN AL, 05h ; Here 05h is a input port number
or indirect addressing
  OUT DX, AL ; DX contains the address of I/O port
Only DX register can be used to point a I/O port

## Slide 15: 5. Implied Addressing
No explicit address is given with the instruction
implied within the instruction itself
Examples:
CLC ; clear carry flag
HLT ; halts the program
RET ; return to DOS

## Slide 16: Dept. of Computer Science and Engineering BRAC University CSE 341 Team
8086 Machine Codes

## Slide 17: Instruction template
For 8085: Just look up the hex code for each instruction.
For 8086 it is not simple.
E.g 32 ways to specify the source in MOV CX, source.
MOV CX, source
Each of these 32 instructions require different binary code.
Impractical to list them all in a table.
Instruction templates help code the instruction properly.
a 16-bit register (8 in number)
a memory location (24 possible memory addressing modes)

## Slide 18: Instruction template (6 bytes)
LOW BYTE DISPLACEMENT / DATA |  |  |  |  |  |  |  | HIGH BYTE DISPLACEMENT / DATA |  |  |  |  |  |  | 
BYTE 3
BYTE 4
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
BYTE 1
BYTE 2
LOW BYTE of IMMEDIATE DATA |  |  |  |  |  |  |  | HIGH BYTE of IMMEDIATE DATA |  |  |  |  |  |  | 
BYTE 5
BYTE 6
An instruction after conversion can have 1 to 6 bytes long of machine code

## Slide 19: Constructing Machine Codes for 8086
Each instruction in 8086 is associated with the binary code.
You need to locate the codes appropriately.
Most of the time this work will be done by assembler
The things needed to keep in mind is:
    Instruction templates and coding formats
    MOD and R/M Bit patterns for particular instruction

## Slide 20: MOV Instruction Coding
MOV data from a register to a register/to a memory location or from a memory location to a register. (Operation Code of MOV: 100010)

## Slide 21: MOD and R/M Field
2-bit Mode (MOD) and 3-bit Register/Memory (R/M) fields specify the other operand.
Also specify the addressing mode.

## Slide 22: MOD and R/M Field
If the other operand in the instruction is also one of the eight register then put in 11 for MOD bits in the instruction code.
If the other operand is memory location, there are 24 ways of specifying how the execution unit should compute the effective address of the operand in the main memory.
If the effective address specified in the instruction contains displacement less than 256 along with the reference to the contents of the register then put in 01 as the MOD bits.
If the expression for the effective address contains a displacement which is too large to fit in 8 bits then out in 10 in MOD bits.

## Slide 23: REG Field
REG field is used to identify the register of the one operand

## Slide 24: Instruction template
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
BYTE 1
BYTE 2
MOV [BX + 34h ], AL
MOV AX, 1234 h
6 bits of
MOV, ADD etc
D - direction If D=0, then direction is from a register (source) If D=1, then direction is to a register (destination)
W - word If W=0, then only a byte is being transferred (8 bits)
If W=1, them a whole word is being transferred (16 bits)
MOV AX, [BX]
MOV AX, [BX + 12h]
MOV AX, [BX + 1234h]
MOV AX, BX
MODE | OPERAND NATURE
00 | Memory with no displacement
01 | Memory with 8-bit displacement
10 | Memory with 16-bit displacement
11 | Both are registers
34h here is an 8-bit displacement
[BX+34h] is a memory/offset address
1234h here is a 16-bit immediate data value

## Slide 25: Instruction template
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
BYTE 1
BYTE 2
Check column that matches with MOD value
Value for R/M with corresponding MOD value
Value for REG with corresponding W value and the register considered in D

## Slide 26: Example 1
MODE | OPERAND NATURE
00 | Memory with no displacement
01 | Memory with 8-bit displacement
10 | Memory with 16-bit displacement
11 | Both are registers
MOV 8B43H [SI], DH: Copy a byte from DH to memory with 16 bit displacement given the opcode for MOV=100010
MOV [SI + 8B43H] , DH
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
BYTE 1
BYTE 2
1 | 0 | 0 | 0 | 1 | 0
source
0
-- 8 bits (not a word size)
0
1 0
Therefore D=0
Therefore W=0
LOW BYTE DISPLACEMENT / DATA |  |  |  |  |  |  |  | HIGH BYTE DISPLACEMENT / DATA |  |  |  |  |  |  | 
BYTE 3
BYTE 4

## Slide 27: Example 1
MOV 8B43H [SI], DH: Copy a byte from DH to memory with 16 bit displacement given the opcode for MOV=100010
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
BYTE 1
BYTE 2
1 | 0 | 0 | 0 | 1 | 0
0
0
1 0
1 | 1 | 0
MOV [SI + 8B43H] , DH

## Slide 28: Example 1
MOV 8B43H [SI], DH: Copy a byte from DH to memory with 16 bit displacement given the opcode for MOV=100010
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
BYTE 1
BYTE 2
1 | 0 | 0 | 0 | 1 | 0
0
0
1 0
1 | 1 | 0
1 | 0 | 0
MOV [SI + 8B43H] , DH

## Slide 29: Example 1
MOV 8B43H [SI], DH: Copy a byte from DH to memory with 16 bit displacement given the opcode for MOV=100010
MOV [SI + 8B43H] , DH
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
LOW BYTE DISPLACEMENT |  |  |  |  |  |  |  | HIGH BYTE DISPLACEMENT |  |  |  |  |  |  | 
BYTE 1
BYTE 2
BYTE 3
BYTE 4
1 | 0 | 0 | 0 | 1 | 0
0
0
1 0
1 | 1 | 0
1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0
1 1
1 | 0 | 0 | 0 | 1 | 0
1 1
Machine Code: 1000 1000 1011 0100 0100 0011 1000 10112 or 88 B4 43 8B16

## Slide 30: Example 2
MODE | OPERAND NATURE
00 | Memory with no displacement
01 | Memory with 8-bit displacement
10 | Memory with 16-bit displacement
11 | Both are registers
MOV AX, BX
destination
-- 16 bits (a word size)
MOV AX, BX: given the opcode for MOV=100010
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
BYTE 1
BYTE 2
1 | 0 | 0 | 0 | 1 | 0
1
1
1 1
AX is 16-bit long,
therefore W = 1
AX considered which is a destination operand,
therefore D = 0

## Slide 31: Example 2
MOV AX, BX: given the opcode for MOV=100010
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
BYTE 1
BYTE 2
1 | 0 | 0 | 0 | 1 | 0
1
1
1 1
0 | 0 | 0

## Slide 32: Example 2
MOV AX, BX: given the opcode for MOV=100010
OPCODE |  |  |  |  |  | D | W | MOD |  | REG |  |  | R/M |  | 
BYTE 1
BYTE 2
1 | 0 | 0 | 0 | 1 | 0
1
1
1 1
0 | 0 | 0
0 | 1 | 1
Machine Code: 1000 1011 1100 00112 or 8B C316

## Slide 33: QUIZ
Compute the machine code for the following using the table below and the opcode for MOV as100010
a) MOV AX, 5E9Ch b) MOV DH, [BP+SI+7Dh]

## Slide 34: Instruction Template
The Intel literature shows two different formats for coding 8086 instructions.
Instruction templates helps you to code the instruction properly.
Example:
IN AL, 05H

## Slide 35: Example

## Slide 36: Example
MOV 43H [SI], DH: Copy a byte from DH register to memory location.

## Slide 37: Example 3
MOV CX, [437AH]: Copy the contents of the two memory locations to the register CX.

## Slide 38: QUIZ
Compute the machine code for the following using the table below and the opcode for MOV as100010
a) MOV AX, 5E9Ch b) MOV DH, [BP+SI+7Dh]

## Slide 39: Thank You !!!