## Slide 1
80286
Microprocessor
Course ID: CSE - 341
Course Title: Microprocessors
Department of Computer Science and Engineering
BRAC University

## Slide 2: 80186
80186 is a 16 bit microprocessor with 16 bit data bus and 20 bit address bus similar to 8086.
80186 has several additional functional chips:
  clock generator
  2 independent DMA channels
  PIC
  3 programmable 16-bit timers
more a microcontroller than a microprocessor
used mostly in industrial control applications

## Slide 3
80286

## Slide 4: Comparison between 8086 and 80286
1. 16 bit microprocessor | 1. 16 bit microprocessor
2. Data bus is 16 bit (D0 to D15) | 2. Data bus is 16 bit (D0 to D15)
3. Address bus is 20 bit (A0 to A19) | 3. Address bus is 24 bit (A0 to A23)
4. Works in two modes (Minimum and Maximum) | 4. Works in two modes (Real and Virtual protected Mode)
5. Has Multiplexed buses so the number of pins are 40. | 5. Has non-multiplexed buses so the number of pins are 68.
6. Operates between 5 to 10 MHz having standard frequency of 6MHz. So slower than 80286 | 6. Operates in 8 MHz, 10 MHz & 12.5 MHz . So faster than 8086
7. Does not support memory management and protection | 7. High performance microprocessor with memory management and protection
8086
80286

## Slide 5: Intel 80286 has 2 operating modes:
Real Address Mode :
    80286 is just a fast 8086 --- up to 6 times faster
    All memory management and protection mechanisms are disabled
    286 is object code compatible with 8086
Protected Virtual Address Mode
    80286 works with all of its memory management and protection capabilities with the advanced instruction set.
    it is source code compatible with 8086

## Slide 6
80286 INTERNAL ARCHITECTURE

## Slide 7
BUS INTERFACE UNIT

## Slide 8: Address unit

## Slide 9: Bus Interface unit

## Slide 10: Instruction unit

## Slide 11: Execution unit

## Slide 12: Functional Parts
Address unit
Bus Interface unit
Instruction unit
Execution unit

## Slide 13: Address Unit
Calculate the physical addresses of the instruction and data that the CPU want to access
Address lines derived by this unit may be used to address different peripherals.
Physical address computed by the address unit is handed over to the Bus Unit.

## Slide 14: Bus Interface Unit
Performs all memory and I/O read and write operations.
Take care of communication between CPU and a coprocessor.
Transmit the physical address over address bus A0 – A23.
Prefetcher module in the bus unit performs this task of prefetching.
Bus controller controls the prefetcher module.
Fetched instructions are arranged in a 6 – byte prefetch queue.

## Slide 15: Instruction Unit
Receive arranged instructions from 6 byte prefetch queue.
Instruction decoder decodes up to 3 prefetched instruction and are latched them onto a decoded instruction queue.
Output of the decoding circuit drives a control circuit in the Execution unit.

## Slide 16: Execution unit
EU executes the instructions received from the decoded instruction queue sequentially.
Contains Register Bank.
contains one additional special register called Machine status word (MSW) register --- lower 4 bits are only used.
ALU is the heart of execution unit.
After execution ALU sends the result either over data bus or back to the register bank.

## Slide 17: Register organization of 80286
The 80286 CPU contains the same set of registers, as in 8086.
  Eight 16-bit general purpose registers.
  Four 16 bit segment registers.
  One Flag register.
  One Instruction pointer.
plus
  one new 16-bit machine status word (MSW) register

## Slide 19: Flag Register

## Slide 20: IOPL – Input Output Privilege Level flags (bit D12 and D13)
Most Privilege
Level
PL = 0
PL=3
PL=2
PL=1
IOPL=00 = 0
IOPL=01 =1
IOPL=10 =2
IOPL=11= 3

## Slide 21: NT – Nested task flag (bit D14)
  When set, it indicates that one system task has invoked another through a CALL instruction as opposed to a JMP.
  For multitasking this can be manipulated to our advantage

## Slide 22: IOPL – Input Output Privilege Level flags (bit D12 and D13)
  IOPL is used in protected mode operation to select the privilege level for I/O devices. If the current privilege level is higher or more trusted than the IOPL, I/O executed without hindrance.
  If the current privilege level is lower than the IOPL, an interrupt occurs, causing execution to suspend.
  Note that IOPL 00 is the highest or more trusted; and IOPL 11 is the lowest or least trusted.

## Slide 23: Machine Status Word Register
Consist of four flags
  PE,
  MP,
  EM and
  TS

## Slide 24: Machine Status Word...

## Slide 25
PE - Protection enable
    Protection enable flag places the 80286 in protected mode, if set. This can only be cleared by resetting the CPU.
MP – Monitor processor extension
    Flag allows WAIT instruction to generate a processor extension.

## Slide 26
EM – Emulate processor extension flag:
if set , causes a processor extension absent exception and permits the emulation of processor extension by CPU.
TS – Task switch: if set, this flag allows task switching and if TS=0 there is no task switching. Task switching means the operating system switches from one task to another.

## Slide 27
80286 ADDRESS TRANSLATION-SEGMENTATION

## Slide 28: Operating Modes of 80286
80286 operates in either the
  real or
  protected mode.
Real mode operation allows addressing of only the first 1M byte of memory space—even in Pentium or Core2 microprocessor.
  the first 1M byte of memory is called the real memory, conventional memory, or DOS memory system

## Slide 29: Why is this Real Mode there?
Protected Mode cannot be entered directly
To work in protected mode, various system tables are required. They are:
Global Descriptor Table
Local Descriptor Table
Page Tables

## Slide 30: Segments and Offsets
All real mode memory addresses must consist of a segment address plus an offset address.
  segment address defines the beginning address of any 64K-byte memory segment
  offset address selects any location within the 64K byte memory segment

## Slide 31: Protected Mode:
In real mode, PE=0
When PE=1, 80286 enters into protected mode
Then it continues to work in protected mode till the time processor is turned off
Thus, after entering into protected mode, PE bit cannot be made 0.
In protected mode, the calculation of physical address is different than that of real mode.

## Slide 32: Protected Mode: Virtual Address
Virtual address is the combination of segment address and offset address.
Segment address tells which segment will be accessed. So, from segment address, the number of segments are to be known.
Offset address tells the location within the segment and from it the maximum size of the segment is known

## Slide 33: Descriptor
There are mainly the LDT and GDT
Global descriptors contain segment definitions that apply to all programs.
Local descriptors are usually unique to an application.
  a global descriptor might be called a system descriptor, and local descriptor an application descriptor

## Slide 34: Contents of segment register
Segment descriptors are each 8k bytes

## Slide 35: 80286 Address Translation- Segmentation
OFFSET(16)
GDT/LDT
Target Segment
Target Location
Base
Limit
Access Right
+

## Slide 36: PROTECTED MODE MEMORY ADDRESSING
Protected mode is where Windows operates.
In place of a segment address, the segment register contains a selector that selects a descriptor from a descriptor table.
The descriptor describes the memory segment’s location, length, and access rights.

## Slide 37
Descriptors are chosen from the descriptor table by the segment register.
  register contains a 13-bit selector field, a table selector bit, and requested privilege level field
The TI bit selects either the global or the local descriptor table.
Requested Privilege Level (RPL) requests the access privilege level of a memory segment.
  If privilege levels are violated, system normally indicates an application or privilege level violation

## Slide 38: Selectors and Descriptors
The selector, located in the segment register, selects one of 8192 descriptors from one of two tables of descriptors.
Descriptor describes the location, length, and access rights of the segment of memory.
In protected mode, this segment number can address any memory location in the system.
Indirectly, the segment register still selects a memory segment, but not directly as in real mode.

## Slide 39
Global descriptors contain segment definitions that apply to all programs.
Local descriptors are usually unique to an application.
  a global descriptor might be called a system descriptor, and local descriptor an application descriptor
The global descriptor table’s base address is stored in GDTR
The local descriptor table’s base address is stored in LDTR
The two privileged instructions LGDT and LLDT loads the GDTR and LDTR.

## Slide 40
80286
Descriptor

## Slide 41: The 80286 descriptors

## Slide 42: The 80286 descriptors
The 80286 descriptor has 3 parts:
1) Limit:
16-bit limit or size allows memory segment lengths of maxm 64K bytes.
2)Base:
The base address of the descriptor indicates the starting location of the memory segment.
  the paragraph boundary limitation is removed in protected mode
  segments may begin at any address
3) Access rights byte:
It controls access to the protected mode segment.
  describes segment function in the system and allows complete control over the segment
  if the segment is a data segment, the direction of growth is specified

## Slide 43: Access Right Byte

## Slide 44: Access Right Byte --- Bit 7 Present?
P
P=1 Valid Descriptor info, Segment is mapped into physical memory
P=0 Descriptor is undefined, no mapping to physical memory exists

## Slide 45: Access Right Byte --- Bit 5,6 Privilege Level
P
DPL
Sets the Descriptor privilege level necessary for protection

## Slide 46: Access Right Byte --- Bit 4 Descriptor Type
P
DPL
S
S=0 System descriptor
S=1 Application Descriptor

## Slide 47: Access Right Byte --- Bit 3 Executable?
DPL
E
S
P
E=0 No Data/Stack Segment
E=1 YES Code Segment

## Slide 48: Access Right Byte
E=0
E=1
ED
C
DPL
S
P
C=1 Ignore DPL
C=0 Abide by DPL
ED=0 Segment expands upward (Data segment)
ED=1 Segment expands downward (Stack Segment)
Bit 2

## Slide 49: Access Right Byte --- Bit 1
DPL
S
P
E=0
E=1
ED
C
W
R
R=0 Code Segment execute only, not readable
R=1 Code Segment both executable & readable
W=0 Data segment not writable
W=1 Data segment writable

## Slide 50: Access Right Byte --- Bit 0 Accessed?
DPL
S
P
E=0
E=1
ED
C
W
R
A
A=0 Segment not accessed
A=1 Segment has been accessed

## Slide 51: 80286 Protection

## Slide 52: Protection Mechanism
There are three checks in protection mechanism:
Limit Check
Type Check
Privilege Check

## Slide 53: Limit Check
Offset is compared with the limit
For 8 bit data,
Offset < = Limit
For 16 bit data,
Offset < = Limit - 1

## Slide 54: Type Check
S E ED W
Or
S E C R
DESCRIPTOR BITS

## Slide 55: Privilege Check

## Slide 56: Privilege Check
Descriptor Privilege Level (DPL) – It is the privilege level of the segment to be accessed. It is there in the target segment descriptor.
Request Privilege Level (RPL) – It is the privilege level of the program to be executed.
Current Privilege Level (CPL) – It is there in the code segment register that is currently running.
Effective Privilege Level (EPL) – Max (CPL,RPL)

## Slide 57: Privilege Check
Privilege Check
CPL
RPL
EPL
DPL
Segment Address
Target Segment
Descriptor
CS Descriptor
Target DPL>= EPL

## Slide 58: Privilege levels and Protection
Every segment has an associated privilege level and hence any code segment will have an associated privilege level.
The CPL (Current Privilege Level) of a process is the privilege level of the code segment, the code stored in which, it is executing.
A process can access segments that have privilege levels numerically greater than or equal to (less privileged than) its CPL.

## Slide 59: Thank You !! and